## Slide 1: Authentic Execution in Smart Farming
Student: Gianluca Scopelliti
Supervisors: Frank Piessens, Jan Tobias Mühlberg, Fritz Alder

## Slide 2: Smart Farming

## Slide 3: What is Smart Farming?
Application of modern ICT in agriculture
Embedded devices connected to:
  Sensors, to collect data from the physical world (e.g. temperature, humidity, light…)
  Actuators, to perform operations to the physical world (e.g. irrigation, animal feeding…)
Central servers to store data and execute software for computing statistics and/or predictions

## Slide 4: Why?
In general, the goal is to maximize profits and minimize costs
The data collected is processed by servers using specialized software, providing to the farmer statistics and support for decisions
  Typically, the farmer interacts with the system through a dashboard
The main benefits of using this approach are:
  Improve input efficiency, by applying the optimal amount of nutrients, seed or chemical products such as pesticides at the right location and time, using the right type of product
  Identify anomalies such as diseases, by analyzing the general health of the crop and livestock
  Reduce labor time and costs, by using actuators and specialized software for performing operations with limited human intervention

## Slide 5: Threats to Precision Agriculture
Paper released by US Department of Homeland Security (DHS) in 2018
“[…] addresses the security threats related to the adoption and impact of new digital technologies in crop and livestock production.”

## Slide 6: Security issues
Confidentiality
  Theft of data
  Leak of data
  Foreign access to data
Integrity
  Manipulation of data
  Introduction of fake data
  Manipulation of actuators
Availability
  Block / alter nodes
  Block / alter communication between nodes

## Slide 7: Trusted Computing and Authentic Execution

## Slide 8: Trusted Computing
Technology developed by the Trusted Computing Group
Goal: provide strong guarantees that a software will not misbehave
  Even in a system where all the other components (OS, other SW) are untrusted!
Key concepts:
  Endorsment Key: unique private key that never leaves the hardware
  Memory curtaining: isolation of sensitive areas of memory
  Sealed storage: bind data to a specific device or software
  Remote attestation: authenticate hw / sw configuration to a remote host
  Trusted third party: an intermediary to provide (ano|pseudo)nymity
In practice we have many different architectures which implement a subset of these features, and they also provide new features such as Enclaved execution and secure I/O

## Slide 9: VulCAN
An application of Trusted Computing in the automotive context
Force points:
  Message authentication
  Software component attestation and isolation

## Slide 10: Authentic Execution
«if the application produces a physical output event (e.g.,
turns on an LED), then there must have happened a sequence of physical input
events such that that sequence, when processed by the application (as specified
in the high-level source code), produces that output event. »
SM 1
SM 2
OUTPUT:
buttonPressed()
INPUT:
incrementCounter()
Event Manager
(UNTRUSTED!)
Connection

## Slide 11: Limitations of the current implementations
VulCAN handles a specific communication medium (CAN)
  The code is then adapted for dealing with its characteristics
    Broadcast network
    64-bit packets (-> MAC truncation)
    …
The current implementation of Authentic Execution manages only Sancus devices
  What about different architectures like SGX?

## Slide 12: My Master’s Thesis

## Slide 13: My Master’s Thesis work
Generalize the concept of Authentic Execution
  Communication medium: provide a sort of generic API which abstracts the network layer
    Goal: the code written by the developer should be transparent to the communication medium used
    The developer has only to specify the technology used and its parameters in a configuration file
  Different architectures: provide support for another architecture (Intel SGX)
    Goal: we want to simulate a system composed by heterogeneous components (from lightweight IoT devices to desktop/server architectures)
      Many real scenarios present such situation (e.g. Smart Farming)

## Slide 14: A prototype: Authentic Execution for automatic irrigation
Goal: apply the concepts described in the previous slide to a concrete use case in the context of Smart Farming

## Slide 15: Schedule
Within the holidays: completing the reading / planning phase
From January onwards: implementation phase
  Authentic execution between two SGX enclaves
  Authentic execution in a heterogeneous system (SGX + Sancus)
  Generic API for the communication

## Slide 16: Conclusions

## Slide 17: Conclusions
Goal: Create a system which provides strong security properties in presence of malicious actors
  Confidentiality, integrity features
Application in a specific context (smart farming)..
  .. but can be also applied to any other areas with different:
    Architectures
    Communication mediums

## Slide 18: References
Threats to Precision Agriculture
Tutorial dsn18 slides
Article about Smart Farming
VulCAN
Authentic Execution
Image slide 3
Image slide 6